## Slide 1
COMPUTER NETWORK SETUP
Teaching Notes
ICT Technician · Level 6 · Sample Technical Training Institute · A. Sample

## Slide 2
Unit information
Unit title: Computer Network Setup
Unit code: 0612 351 03A
Course: ICT Technician
Level: 6
College: Sample Technical Training Institute
Prepared by: A. Sample
Learning outcomes: 3
Total hours: 200

## Slide 3
Course outline
LO 1: Terminate computer network cables
LO 2: Connect computer network cables
LO 3: Perform computer network maintenance

## Slide 4
Learning Outcome 1
TERMINATE COMPUTER NETWORK CABLES

## Slide 5
What you will learn
By the end of this outcome you will be able to select the correct devices, media and tools for a cabling job,…
Notes: By the end of this outcome you will be able to select the correct devices, media and tools for a cabling job, and terminate UTP cable onto RJ-45 connectors, outlets and patch panels to TIA/EIA-568, testing every termination you make.

## Slide 6
Network types and topologies
A network is classified first by the area it covers and then by the shape in which its nodes are joined
Star — every node has its own cable back to a central switch
Bus — all nodes tap one backbone terminated at both ends
Ring — nodes form a closed loop
Mesh — multiple redundant paths between nodes
Notes: A network is classified first by the area it covers and then by the shape in which its nodes are joined. A LAN covers one building or site and is owned by the organisation; a WAN spans towns or countries and usually rides on a service provider's links; a MAN sits between the two, across a city. The topology is the arrangement of the nodes, and it decides how a fault spreads.

## Slide 7
Network types and topologies (cont.)
Hybrid — real installations are usually a star at each floor, joined into a tree by the backbone
Example: A 24-user office: one switch in a floor cabinet, one cable per desk — a star
Example: Three floors, each with its own switch, all uplinked to a core switch in the server room — a tree of stars
Example: Two core switches cross-linked to both distribution switches so either can fail — a partial mesh

## Slide 8
Transmission media and when to use each
Media choice is decided by distance, the electrical environment and the bandwidth you must carry
UTP — four unshielded twisted pairs
STP/FTP — the same pairs with a foil or braid screen and a drain wire
Fibre — light in a glass core
Category matters: Cat 5e to 1 Gbps, Cat 6 to 10 Gbps over short runs, Cat 6A to 10 Gbps over the…
Notes: Media choice is decided by distance, the electrical environment and the bandwidth you must carry. Getting it wrong is expensive because the horizontal cable is buried in the fabric of the building and is not easily replaced.

## Slide 9
Transmission media and when to use each (cont.)
Example: Desk outlets on all three floors: Cat 6 UTP
Example: The run from the workshop, which passes a welding bay: screened Cat 6A, bonded at both ends
Example: Between the main block and the hostel, 300 m apart: multimode fibre, which also avoids an earth loop between two buildings

## Slide 10
The T568A and T568B pin assignments
TIA/EIA-568 defines which conductor lands on which of the eight pins
T568B, pins 1 to 8: white/orange, orange, white/green, blue, white/blue, green, white/brown, brown
T568A, pins 1 to 8: white/green, green, white/orange, blue, white/blue, orange, white/brown, brown
Pins 4, 5, 7 and 8 are identical in both schemes — only pins 1, 2, 3 and 6 move
Both ends the same scheme = straight-through, used between unlike devices (PC to switch)
Notes: TIA/EIA-568 defines which conductor lands on which of the eight pins. Two schemes exist, and they differ only in that the orange and green pairs are swapped. Either is correct; mixing them on the two ends of one cable is what makes a crossover.

## Slide 11
The T568A and T568B pin assignments (cont.)
One end A and the other B = crossover, used between like devices (switch to switch) on equipment without Auto-MDI/MDI-X
Pick one scheme for the whole site — usually T568B in this region — and write it on the documentation

## Slide 12
The T568A and T568B pin assignments — worked example
T568B (pin : conductor)
1 : white/orange 5 : white/blue
2 : orange 6 : green
3 : white/green 7 : white/brown
4 : blue 8 : brown
T568A swaps the orange and green pairs:
1 : white/green 3 : white/orange
2 : green 6 : orange
(pins 4, 5, 7, 8 unchanged)

## Slide 13
Terminating to standard — the four things that fail
Most terminations that fail certification fail for one of four reasons, and all four are workmanship rather than materials
Excessive untwist. More than about 13 mm of untwisted pair at the connector raises near-end crosstalk. Untwist only as far as the…
Split pairs. Each conductor is continuous end to end, but two conductors from different pairs are used as a pair. A continuity…
Conductors not fully seated
Sheath not captured. If the outer sheath does not reach past the strain-relief point, any pull on the cable is taken by…
Notes: Most terminations that fail certification fail for one of four reasons, and all four are workmanship rather than materials. Learn to spot them on your own work before the tester does.

## Slide 14
Terminating to standard — the four things that fail (cont.)
Example: A link that shows a green light but drops under load: usually a split pair or a partly seated conductor
Example: A patch cord that works until someone moves the desk: the sheath was not captured by the strain relief

## Slide 15
Practice activities
Identify and name every tool on the termination bench, and state what each one does
Strip a 300 mm offcut of Cat 6 and measure your strip length with a rule
Lay out the eight conductors in T568B order without looking at the chart, then check yourself
Terminate one end of a cord, then inspect the connector tip against the four failure modes above before you crimp
Swap cords with a partner and test each other's work on the cable tester

## Slide 16
Make and prove three patch cords
The laboratory needs patch cords for a new bench
Cut two 2 m lengths and one 1.5 m length of Cat 6 UTP
Slide a strain-relief boot onto each end before you strip anything — it cannot be fitted after the connector is crimped
Strip 12–13 mm of sheath from each end without nicking the conductors
Terminate both 2 m cords T568B at both ends
Notes: The laboratory needs patch cords for a new bench. You are to make two straight-through cords and one crossover, and prove each one before it is issued.

## Slide 17
Make and prove three patch cords (cont.)
Check the connector tip on every end: all eight conductors visible, sheath past the strain relief
Crimp in one firm stroke, then slide the boot up over the connector
Test all three cords and record the wire map result for each
Label each cord with its type and your name
Expected: Two straight-through cords that map pin 1 to pin 1 through to pin 8

## Slide 18
Make and prove three patch cords (cont.)
Expected: One crossover cord showing the 1–3 and 2–6 transposition on the tester
Expected: A completed test record for all three cords

## Slide 19
Learning checks
Oral: Which four pins differ between T568A and T568B?
Oral: Why does a split pair pass a continuity test but fail certification?
Written: State four network topologies and give one advantage of each
Written: Explain why the untwist at a termination must be kept under 13 mm
Practical: Terminate an RJ-45 connector to T568B and have it pass a wire-map test first time

## Slide 20
Learning checks (cont.)
Practical: Identify, from a set of pre-made cords, which is straight-through and which is crossover, using the tester

## Slide 21
Revision and self-check
Revise by making cords until you pass first time without checking the colour chart
Written test
Practical assessment
Direct observation
Oral questioning
Notes: Revise by making cords until you pass first time without checking the colour chart. Being able to recite the pin order is not the competency — producing a termination that certifies is. Keep every test record; the assessor will ask to see it.

## Slide 22
Learning Outcome 2
CONNECT COMPUTER NETWORK CABLES

## Slide 23
What you will learn
By the end of this outcome you will be able to observe the required safety measures, mount and interconnect network devices to…
Notes: By the end of this outcome you will be able to observe the required safety measures, mount and interconnect network devices to a design, route and dress cable to standard, apply an IP addressing scheme, and verify that the network you have built works.

## Slide 24
Safety on a network installation
Cabling work puts you in ceilings, under floors and inside cabinets that may be live
Wear the PPE issued: dust coat, safety glasses when cutting or drilling, gloves when handling cable trays
Isolate and lock off power before working inside a cabinet or trunking that carries mains
Never look into the end of a fibre or a fibre port
Barrier and sign any open floor box, lifted tile or ladder
Notes: Cabling work puts you in ceilings, under floors and inside cabinets that may be live. The safety measures are not generic advice — they are performance criteria you will be assessed on, and the assessor will stop a practical for an unsafe act.

## Slide 25
Safety on a network installation (cont.)
Use a tested ladder or platform
Report damaged tools and take them out of service rather than working round the fault

## Slide 26
Mounting and dressing — why it is marked
A cabinet that is neat is not just tidy; it is maintainable
Put patch panels immediately above or below the switch they serve, so patch cords are short and do not cross the cabinet
Heavy items — UPS, servers — go at the bottom, or the rack becomes unstable
Leave clearance for airflow, and respect the fan direction
Keep power leads on one side and data cords on the other, crossing at right angles if they must cross
Notes: A cabinet that is neat is not just tidy; it is maintainable. Marks are awarded for the arrangement because the arrangement is what a technician has to work with three years later at two in the morning.

## Slide 27
Mounting and dressing — why it is marked (cont.)
Support cables with hook-and-loop straps, not over-tightened cable ties — a tight tie deforms the pairs and shows up as a certification…
Respect the bend radius, typically four times the cable diameter for UTP, and do not fill trunking beyond about 40 %

## Slide 28
IP addressing and subnetting
Every device on the network needs an address, a mask that tells it which addresses are local, and a gateway for everything…
An IPv4 address is 32 bits, written as four octets
Usable hosts in a subnet = 2^(host bits) − 2
Borrowing n bits from the host part creates 2^n subnets
Private ranges: 10.0.0.0/8, 172.16.0.0/12 and 192.168.0.0/16
Notes: Every device on the network needs an address, a mask that tells it which addresses are local, and a gateway for everything else. Subnetting borrows host bits to create more, smaller networks — usually to separate departments, or to keep broadcast domains small.

## Slide 29
IP addressing and subnetting (cont.)
Give servers, printers and network devices static addresses; give workstations DHCP addresses from a pool that excludes the static range
Document the plan before you configure anything

## Slide 30
IP addressing and subnetting — worked example
Worked example — divide 192.168.20.0/24 into four subnets
Borrow 2 host bits -> /26 mask 255.255.255.192
Subnets = 2^2 = 4
Hosts = 2^6 - 2 = 62 usable per subnet
Subnet 1 192.168.20.0/26 hosts .1 - .62 broadcast .63
Subnet 2 192.168.20.64/26 hosts .65 - .126 broadcast .127
Subnet 3 192.168.20.128/26 hosts .129 - .190 broadcast .191
Subnet 4 192.168.20.192/26 hosts .193 - .254 broadcast .255

## Slide 31
Verifying the network you have built
You have not finished when the cables are in
Link light at the NIC and at the switch port — proves the physical link
ipconfig / ifconfig — proves the device has the address you intended, not an APIPA 169.254 address from a failed DHCP
ping the loopback (127.0.0.1) — proves the TCP/IP stack on the machine itself
ping a peer on the same subnet — proves local switching
Notes: You have not finished when the cables are in. You have finished when you can show, and record, that traffic passes. Work outwards from the node: prove each layer before moving to the next.

## Slide 32
Verifying the network you have built (cont.)
ping the gateway — proves the route off the subnet
ping an external host by name — proves routing and DNS together
Record each result against the outlet label on the test schedule
Example: Address is 169.254.x.x: the machine never reached a DHCP server — check the cable, the port and the VLAN before blaming the…
Example: ping 8.8.8.8 works but ping google.com fails: routing is fine, DNS is not configured or unreachable

## Slide 33
Practice activities
Mount a patch panel and switch in a practice cabinet and dress six patch cords through the management bars
Given a floor plan and a user count, write an addressing plan before touching a device
Subnet 10.10.0.0/16 for six branches of up to 500 hosts each, and justify your choice of mask
Configure two workstations and prove connectivity through the full ping sequence, recording each step
Introduce a deliberate duplicate address on a partner's bench and watch what the symptom looks like

## Slide 34
Build and prove a small office network
You are handed a switch, a router, two workstations, a patch panel and the cabling you terminated in Outcome 1
Mount the patch panel and switch in the cabinet, observing position, airflow and cable management
Patch the two horizontal runs to the switch and uplink the switch to the router's LAN port
Write an addressing plan for both workstations, the switch management interface and the router from 192.168.50.0/24
Configure the addressing on each device
Notes: You are handed a switch, a router, two workstations, a patch panel and the cabling you terminated in Outcome 1. Build a working network and prove it.

## Slide 35
Build and prove a small office network (cont.)
Run the verification sequence from each workstation: link light, ipconfig, loopback, peer, gateway, external host
Record every result on the test schedule, then label the patch cords and update the patch record
Expected: A written addressing plan with no duplicate addresses, produced before configuration
Expected: Both workstations reaching each other, the switch, the router and an external host
Expected: A completed test schedule and an updated patch record

## Slide 36
Learning checks
Oral: Why do we subtract two when calculating usable hosts in a subnet?
Oral: What does a 169.254 address tell you?
Written: State five safety measures observed when working on a network installation in an occupied office
Written: Divide 192.168.20.0/24 into four subnets and give the mask, usable hosts and the four network addresses
Practical: Build a star network from the components supplied and demonstrate connectivity to the assessor

## Slide 37
Learning checks (cont.)
Practical: Apply a supplied addressing plan and prove there are no duplicates

## Slide 38
Revision and self-check
The verification sequence is what separates a pass from a fail here
Written test
Practical assessment
Direct observation
Project work
Notes: The verification sequence is what separates a pass from a fail here. Anyone can plug cables in; the competency is proving, in order, that each layer works and recording the evidence. Practise until the sequence is automatic.

## Slide 39
Learning Outcome 3
PERFORM COMPUTER NETWORK MAINTENANCE

## Slide 40
What you will learn
By the end of this outcome you will be able to select and use network monitoring tools, monitor performance against a plan,…
Notes: By the end of this outcome you will be able to select and use network monitoring tools, monitor performance against a plan, diagnose faults using a structured procedure, repair or replace faulty components, and document the work to workplace standard.

## Slide 41
Monitoring tools and what each one tells you
Different tools answer different questions
Cable tester / certifier — wire map, length, attenuation, crosstalk
Link lights and switch port statistics — CRC errors, discards, speed and duplex
ping and traceroute — reachability and where in the path the loss starts
Protocol analyser (Wireshark) — the actual packets
Notes: Different tools answer different questions. Reaching for the wrong one wastes time; a protocol analyser will not tell you that a cable is broken, and a cable tester will not tell you that a link is congested.

## Slide 42
Monitoring tools and what each one tells you (cont.)
SNMP monitoring platform — utilisation, uptime and error counters over time
Bandwidth monitor — throughput per link

## Slide 43
Monitoring against a plan
Monitoring only means something against a baseline
Baseline utilisation on each uplink at a typical busy hour, and record it
Watch error counters, not just utilisation — rising CRC errors on one port almost always mean a cable, connector or duplex mismatch…
Track latency to the gateway and to an external host
Record device uptime. A switch that reboots on its own has a power or hardware fault, whatever else it is doing
Notes: Monitoring only means something against a baseline. Take readings when the network is known-good, and the same readings later tell you what has changed.

## Slide 44
Monitoring against a plan (cont.)
Set thresholds and alert on them, so the first person to notice a problem is not the user

## Slide 45
A structured diagnostic procedure
Faults are found by narrowing the field, not by guessing
Confirm the symptom yourself
Establish the scope: one node, one port, one switch, one floor, or everything
Check the physical layer first: link lights at both ends, cable seated, patch cord not damaged
Substitute a known-good component — cord, port, workstation — to isolate the faulty one
Notes: Faults are found by narrowing the field, not by guessing. Work from the symptom outwards, and change one thing at a time so you know which change fixed it.

## Slide 46
A structured diagnostic procedure (cont.)
Move up the stack: addressing (ipconfig), local reachability (ping peer), gateway, DNS
Once found, fix it, then prove the fix by repeating the test that failed
Document the fault, the diagnosis, the action and the verification

## Slide 47
A structured diagnostic procedure — worked example
Symptom: one workstation has no access, its neighbours are fine
1 Link light at NIC and at the switch port? no -> physical
2 Swap the patch cord for a known-good one fixed -> cord
3 ipconfig -> 169.254.x.x ? yes -> DHCP path
4 ping 127.0.0.1 fail -> local stack
5 ping peer on same subnet fail -> switching / VLAN
6 ping gateway fail -> routing / gateway
7 ping 8.8.8.8 then a hostname name only fails -> DNS
8 Record fault, cause, fix and verification in the log

## Slide 48
Repair, replacement and the maintenance record
Replacing a component on a live network is a planned operation, not a reflex
Schedule disruptive work in an agreed window and tell the users first
Back up the configuration and record the port assignments before you touch anything
Label every cord before disconnecting
Isolate power and observe ESD precautions when handling boards and modules
Notes: Replacing a component on a live network is a planned operation, not a reflex. The record you leave behind is part of the job.

## Slide 49
Repair, replacement and the maintenance record (cont.)
Restore the configuration, reconnect to the labelled ports, and verify every port comes up
Log it: date, fault reported, fault found, action taken, parts and serial numbers, verification result, technician, downtime

## Slide 50
Practice activities
Baseline the laboratory network: record utilisation and error counters on each uplink at a busy time
Work in pairs — one introduces a single fault, the other diagnoses it using the sequence above and times themselves
Read a switch's port statistics and identify the port with a physical problem from the error counters alone
Write a maintenance log entry for a fault you diagnosed, and have a partner check it is complete enough to act on
Draft a maintenance schedule for a 40-user office: what is checked daily, monthly and annually

## Slide 51
Diagnose, repair and document an introduced fault
The assessor introduces one fault into the network you built in Outcome 2
Confirm the symptom and establish its scope before touching anything
Select the monitoring or test tool appropriate to the layer you suspect, and say why you chose it
Work through the diagnostic sequence, explaining each step to the assessor as you carry it out
State the fault and the evidence that led you to it
Notes: The assessor introduces one fault into the network you built in Outcome 2. You must find it, fix it, prove it and record it.

## Slide 52
Diagnose, repair and document an introduced fault (cont.)
Carry out the repair or replacement safely
Repeat the test that originally failed and demonstrate the network is restored
Complete a maintenance log entry covering the fault, diagnosis, action and verification
Expected: A correct diagnosis supported by the evidence you gathered, not by guesswork
Expected: A restored network demonstrated to the assessor by the test that originally failed

## Slide 53
Diagnose, repair and document an introduced fault (cont.)
Expected: A maintenance log entry a colleague could act on without asking you anything

## Slide 54
Learning checks
Oral: Which tool would you reach for first if one port shows rising CRC errors, and why?
Oral: Why do we baseline a network when it is working?
Written: Identify four network monitoring tools and state what each one measures
Written: Set out a structured procedure for diagnosing a workstation with no network access
Practical: Diagnose an introduced fault within the time allowed, explaining each step

## Slide 55
Learning checks (cont.)
Practical: Replace a faulty patch cord or switch port assignment and prove the link is restored

## Slide 56
Revision and self-check
You are marked on the procedure as much as on the answer
Written test
Practical assessment
Direct observation
Oral questioning
Notes: You are marked on the procedure as much as on the answer. A candidate who finds the fault by luck, without a structured search, has not shown the competency. Talk the assessor through your reasoning as you work.

## Slide 57
Revision and self-check (cont.)
Case study

## Slide 58
Set up and hand over a small office network
A six-person office is moving into a new suite
Six horizontal runs terminated at outlets and on the patch panel, all to one scheme
Patch cords made by you, labelled and tested
Switch and patch panel mounted with correct positioning, airflow and cable management
An addressing plan from a private range, with static addresses for infrastructure and a DHCP pool for workstations
Notes: A six-person office is moving into a new suite. It needs six data outlets, a floor cabinet with a patch panel and switch, a router to the ISP service, an addressing plan, and a documentation pack at handover.

## Slide 59
Set up and hand over a small office network (cont.)
Every link tested, with the results recorded against the run labels
A working network with all six outlets live and reaching the internet
A test schedule covering every run and cord
An as-built plan showing outlet positions and their labels
A patch record mapping outlet to panel port to switch port

## Slide 60
Set up and hand over a small office network (cont.)
An addressing plan and an equipment inventory with serial numbers

## Slide 61
Self-check checklist
Select devices, media and tools — Correct category of cable, matching connectors, and serviceable tools selected for the specification
Terminate to TIA/EIA-568 — Untwist within limits, correct colour sequence, all conductors seated, sheath captured
Route and dress cabling — Bend radius respected, trunking not overfilled, data separated from power, cables supported without deformation
Mount and interconnect devices — Panel and switch positioned for short patching and airflow; topology formed as designed
Apply an IP addressing scheme — Plan written before configuration; no duplicates; correct mask and gateway throughout

## Slide 62
Self-check checklist (cont.)
Verify connectivity — Full sequence demonstrated from link light through to an external host, each result recorded
Diagnose a fault — Structured search, one change at a time, conclusion supported by evidence
Document the work — Test schedule, patch record and maintenance log complete and legible

## Slide 63
Written revision questions
State four network topologies and give one advantage of each
Differentiate between UTP, STP and fibre optic media
List the T568B pin assignments from pin 1 to pin 8
State four hand tools used to terminate UTP cable and the purpose of each
Explain why the untwist at a termination must be kept under 13 mm

## Slide 64
Written revision questions (cont.)
State three items of information recorded in a network maintenance log
Describe the T568A and T568B pin assignments and explain the consequence of mixing them on the two ends of a run
Divide 192.168.20.0/24 into four subnets
Explain four rules observed when routing and dressing cables in trunking, giving the reason for each
Set out a structured procedure for diagnosing a workstation that has no network access while its neighbours work normally

## Slide 65
Written revision questions (cont.)
Describe the procedure for replacing a faulty switch in a live network, including the precautions taken

## Slide 66
Oral revision questions
Which four pins differ between T568A and T568B?
Why does a split pair pass a continuity test but fail a wire-map test?
What does a 169.254 address tell you about a workstation?
Why is a bend radius specified for UTP cable?
Which tool would you use first if one switch port shows rising CRC errors?

## Slide 67
Practical revision task
Terminate two horizontal runs, connect them into a working network with two workstations and a router, apply an addressing plan, and diagnose…
Select and check your tools and materials before starting
Terminate both runs to T568B at outlet and patch panel
Make the patch cords you need and test everything you terminate
Mount and interconnect the devices, then apply the addressing plan
Notes: Terminate two horizontal runs, connect them into a working network with two workstations and a router, apply an addressing plan, and diagnose a fault introduced by the assessor.

## Slide 68
Practical revision task (cont.)
Prove connectivity with the full verification sequence and record each result
Diagnose, repair and document the fault the assessor introduces

## Slide 69
References
ANSI/TIA-568 series — Commercial Building Telecommunications Cabling Standard
ISO/IEC 11801 — Information technology: generic cabling for customer premises
Kenya Occupational Safety and Health Act, 2007 — duties when working at height and on electrical installations
Manufacturer's installation instructions for the connectors, outlets and patch panels in use on site
TVET CDACC curriculum for Computer Network Setup, unit code 0612 351 03A